Das2-Pyserver 2.2 - Internal Specifications
Revision 2019-08-23

This document provides for internal specifications for developers of das2-pyserver.

Purpose	Who	Date
Initial Copy-In from das2-pyserver users guide	C. Piker	2019-08-23

Revisions

Dept. Of Physics & Astronomy
The University of Iowa
Iowa City, IA 52242

# Task Database Specification
The program, das2_svr_arbiter, which handles background processing requested by other components of a Das2 server. It produces cache files, generates coverage plots, collects usage statistics, etc. By default the program is run as a daemon listening for job requests from a work queue broker. Currently the only work queue broker supported is the Redis server. Thus all remaining information in this section will assume that Redis is in use.
## Input Work List: das2_todo
After starting, das2_svr_arbiter opens a connection to the Redis server listed in the server configuration file, das2sever.conf, and issues a blocking right pop operation on the list variable, das2_todo. List values strings defining tasks to be handled and have the following format:
req_time|reqester|requester_ex|rmtreq|rmtreq_ex|user|job_cat|job_fields...
Task strings always start with the following sub-fields which are delimited by pipe '|' characters.
1. 0: req_time - An ISO-8601 time and date string to at least seconds resolution, example: 2015-03-25T10:37:43.334
2. 1: requester - An identifier of the program making the request. For example the URL to the das2server associated with the task may be used: http://planet.physics.uiowa.edu/das/das2Server
3. 2: requester_ex - Extra information about the server, may be empty.
4. 3: rmtreq - Some programs, such as web servers handle request on behalf of remote clients. The IP of the client requesting the operation. Note this may the IP of the server itself if a work item was entered via the das2_srv_todo program.
5. 4: rmtreq_ex - Extra information about a client, such as it's GeoIP location, may be empty.
6. 5: user - The user name, if any associated with the work request, may be empty
7. 6: job_cat - The job category, may not be empty. Sections through below list the current job categories and the job-specific fields
8. 7-N: job_fields - Each category of job has it's own list of fields following the job_cat field. See Tables 1 through 3 for a description of each job category and the required fields.
Empty fields are represented by two adjacent pipes with no intervening characters. To make the protocol expandable, each job category has it's own field set. These are added at index 7 and continue as far as is dictated by the category.
### Build Cache Task
This task requests a cache build for a specified range of a dataset at one, or all of the resolutions listed in the dataset's DSDF file. This task type is specific to the Das 2.2 system interface. Upcoming Das 2.3 cache tasks will presumably require a different set of fields, or different field values.
Job Category Value: TASK_CACHE
Overall / Field Index	Job / Field Name	Job Field Description
7	dataset	The name of the dataset that needs to be cached. This is always the relative DSDF filename without the extension. Examples: juno/wav/survey, voyager/1/pws/SpecAnalyzer-4s-Efield
8	begin_index	The beginning index to cache, for Das 2.2 this is an ISO-8601 start time.
9	end_index	The ending index to cache, for Das 2.2 servers this is an ISO-8601 end time.
10	cache_level	A requested cache level index. This maybe the keyword ALL, to indicate that all cache levels specified in the dataset's DSDF file are to be produced, or this may be one of the given cache index values. See the cacheLevels_XX DSDF value in Section 3.2 of the Das 2.2.1 ICD. Leading zeros are ignored.

Table 1: TASK_CACHE - Task Specific Fields
The following string provides an example of a cache_2.2 task request:
2015-03-25T10:37:43.334|jupiter||128.255.33.104|US,Iowa,Iowa City||TASK_CACHE| juno/fgm/MagComponentsSCSE||2014-01-01|2014-01-02|ALL
### Record Access Task
Job Category Value: TASK_USAGE
Access event tasks are meant to record which datasets are being retrieved. The Job specific fields are given in Table 2 below.
Overall / Field Index	Job / Field Name	Job Field Description
7	dataset	The name of the dataset that needs to be cached. This is always the relative DSDF filename without the extension. Examples: juno/wav/survey, voyager/1/pws/SpecAnalyzer-4s-Efield
8	begin_index	The beginning index to cache, for Das 2.2 this is an ISO-8601 start time.
9	end_index	The ending index to cache, for Das 2.2 servers this is an ISO-8601 end time.
10	params / (optional)	A non-indexing parameter string. Some readers take parameters that are not part of the start and stop period of the data cache.
11	resolution	The floating point resolution datum requested from the client, or empty if no specific resolution was specified.
12	interval	Some datasets are produced at required intervals only. If such a dataset was accessed this field records the interval, otherwise it is blank.

Table 2: TASK_USAGE - Task Specific Fields
The following string provides an example of an access log request for the Voyager spectrum analyzer distogram reader:
2015-03-25T10:37:43.334|planet||128.255.33.104|US,Iowa||TASK_USAGE| voyager/1/pws/SpecAnalyzer-Distogram|2011-07-24|2011-08-31|10 10|340.0 s|
### Update Coverage Plot
Job Category Value: TASK_COVERAGE
PyServer can provide dataset coverage plots, this work item request an update of those inventory plots.
Overall / Field Index	Job / Field Name	Job Field Description
7	dataset	The name of the dataset whose coverage needs to be updated, or the keyword ALL, to indicate that coverage for all datasets should be updated.
8	begin_index	The beginning time for finding data coverage
9	end_index	The ending time for finding data coverage.

Table 3: TASK_COVERAGE - Job Specific Fields
The following string provides an example of a massive coverage plot update.
2015-03-25T10:37:43.334|planet||128.255.33.71||cwp|TASK_COVERAGE|||1977-01-01|2016-01-01
## In-Process List: das2_working_proc-id
Each instance of das2_srv_arbiter uses a single list to record jobs in process. The current version of the arbiter is single threaded, so at most one item will appear in a das2_working_NNNNN list, it's format is:
req_time|server|server_ex|client|client_ex|user|job_cat|job_specific...|begin|
status|progress

The working list just adds two fields to the end of which-ever job type is in progress. These are:
1. -3: begin - An ISO-8601 time indicating when the job was started.
2. -2: status - Current job status message. (optional)
3. -1: progress - A fraction giving how much of the job is completed, where 1.0 is the entire job. The fraction may be specified as a fraction using the '/' sign to separate two numbers.
4. Here is an example of a coverage plot task item value.
2015-03-25T10:37:43.334|planet||128.255.33.71||cwp|TASK_COVERAGE|||1977-01-01|2016-01-01|2015-03-25T10:37:44.512|Updating cassini/mag/4-vec|32/114
## Result List: das2_finished
Finished items end up in a single list for the entire site. This list persists until cleared by a logger. These items are identical to In-Process items with the exception that the progress value is replaced with an end time.
req_time|server|server_ex|client|client_ex|user|job_cat|job_specific...|begin|status|end|return_code
2. -4: begin - An ISO-8601 time indicating when the job was started.
3. -3: status - End status message. (optional)
4. -2: end - An ISO-8601 time indicating when the job finished.
5. -1: return_code - The finial return code from the handling the work item. To continue the tradition set long ago, 0 indicates success non-zero is a failure code.
2015-03-25T10:37:43.334|planet||128.255.33.71||cwp|TASK_COVERAGE|||1977-01-01|2016-01-01|2015-03-25T10:37:44.512|Generated coverage map for all 114 datasets.|2015-03-29T01:14:55.512|0

# Time Average Data Cache Specification
Typically Das2 Servers exist to feed data to graphical clients. In many situations the data stored on disk are more detailed that an application can display. Take for example a magnetometer than produces one measurement every quarter of a second. Typically a scientist will want to view all data for a particular day, or maybe all data for a multi-day orbit. For our hypothetical instrument, a day's measurements are 345,600 data points. Since an average computer screen is only around 2000 pixels wide sending a whole day's worth of measurements at intrinsic resolution is a waste of network bandwidth and client memory.
As part of the Das2 Client-Server protocol (see the Das 2.2 ICD), client programs may inform the server of the minimum resolution that is expected with each data request. To make better use of resources the Das2 servers use the resolution information to reduce data streams on the server before transmission to the remote client. This makes life easier on the client program, however it does nothing to conserve compute resources on the server. All relevant high resolution files must be read by reader programs for each request, and reduction calculations must be re-run for each client request. To solve this problem, the Das2 PyServer can be directed to cache reduced data streams, but to do so in a multi-process environment, a task queue system is needed.

## Cache Layout
The following rules are used by das2_srv_arbiter to store files in the disk cache, and by das2_cache_rdr to read file from the disk cache. These are provided in case that you need to manually manipulate the cache, or for writing replacement cache readers.
Reduced resolution files are found using the following directory path:
CACHE_ROOT / dataset_name / norm_params / res_dir / block_dirs / block_file
Table 4 below breaks out each component of a cache file path.
Path Component	Description	Input Source
CACHE_ROOT	The root of the pre-reduced data file tree	das2server.conf
dataset_name	The dataset name on the server. Note that dataset names are hierarchical. Each section of the name becomes a path component.	client query
param_string	This is a normalized parameter string, thus all spaces and other dangerous components have been transformed into alternate characters. This string does not include the data range query paramentes (typically a begin and end time). See part of this section for normalization rules.	client query
res_dir	This directory corresponds to the resolution of the reduced data. / • For binned data, the name is the prefix bin- concatenated with the resolution value (no units). / • The server can also cache intrinsic resolution data. In this cane the resolution directory is just named 'intrinsic'. This is a useful optimization when dealing with slow reader programs.	dataset DSDF file
block_dirs	These path components are based on the resolution's coverage blocks. For example if the 'daily' coverage blocks are selected for a resolution in the DSDF file then this would be just be a single directory containing the 4-digit year. See part of this section for the available schemes.	dataset DSDF file
block_file	The filename is produced as follows: / coverage_resolution.suffix / where coverage is scheme dependent, resolution is the same string found in the resolution_dir component above, and suffix depends on the file format, either d2s or qds for Das2 streams and QStreams respectively. See part of this section for the available coverage blocks.	dataset DSDF file

Table 4: Cache File Path Components
### Normalized Parameter Strings
todo: document the normalization algorithm

### Available Coverage Blocks
Currently only time series data may be arranged into coverage periods. This meets must current needs but should be expanded to handle measurements such as radar returns that correlate with locations on a planetary surfaces.
Coverage Blocks	Directory Pattern	File Name Prefix	Partial Path Example
persecond	YYYY/MM/DD/HH/MM	YYYY-MM-DDTHH-MM-SS_	2013/10/31/01/05/2013-10-31T01-05-57_bin-10ms.d2s
perminute	YYYY/MM/DD/HH	YYYY-MM-DDTHH-MM_	2013/10/31/01/2013-10-31T01-05_bin-1s.d2s
hourly	YYYY/MM/DD	YYYY-MM-DDTHH_	2013/10/31/2013-10-31T01_bin-1s.d2s
daily	YYYY/MM	YYYY-MM-DD_	2013/10/2013-10-31_bin-60s.d2s
monthly	YYYY	YYYY-MM_	2013/2013-10_bin-3600s.d2s
yearly	(none)	YYYY_	2013_bin-86400s.d2s

Table 5: Times Series Cache Blocks
Das 2.2 servers are heavily targeted towards handling time series data. It is anticipated that new coverage block storage schemes will be needed to handle future Das 2.3 client queries.